## Slide 1
Home Ventilation
1
Background: As Habitat homes are being built more tightly to reduce heat loss, there has been an increasing concern about the amount of fresh air coming into the house.
Objectives:
Determine the desired level of ventilation for a habitat house in Arkansas.
Relate ventilation to blower door test result
Select a few feasible ventilation solutions
Findings:
ASHRAE 62.2 requires 40.5 CFM for 1050 ft2
EnergyStar & ASHRAE require ≥ 5 AHC
continuous or ≥ 100 CFM intermittent for the
kitchen and ≥ 20 CFM continuous or ≥ 50 CFM
intermittent for the bathroom.
The International Energy Conservation Code requires a blower door test result of less than 3 ACH50.
IECC: All homes in zones 3-8 (including Arkansas) will be required to have a whole-house mechanical ventilation system.
David Bell
How air leaks into a house

## Slide 2
Home Ventilation
2

## Slide 3
Solutions:
Bathroom & kitchen exhaust fans
  Requires kitchen fan to run ~50% continuously or 2 bathroom fans to run ~100% continuously
  These fans are generally loud and inefficient
  Doesn’t include air intake, thus creating a negative pressure on the house.
  Requires human control to turn on and off or added control unit
Home Ventilation
Benefits:
HEALTH: Immediate health risks associated with indoor air pollution such as asthma and flu will be reduced. Good air quality also reduces the risk of heart and lung diseases and cancer caused by pollution such as Radon, VOC’s, fuel, and building materials.
SUSTAINABILITY: ERV systems recover energy from exiting air, thus reducing the energy consumption and cost.
COST: Multiple solutions are provided to support a variety of budgets. Each solution has a different operating cost.
DURABILITY: Fresh air reduces the risk of mold and other pollution damage to the house.
ERV such as Trane FreshEffects or Broan ERV
  Good with Arkansas Humidity
  Integration with heat & air control
  Energy efficient
  Cost: ~$1100-$1400 with installation.